## Slide 1: Engineering Mechanics Course code: 116U06C104
Module 4: Equilibrium
Lecture : Introduction to equilibrium of system, types of supports & loads

## Slide 2: Learning Outcomes
Lect 21: At the end of lecture learner will be able to draw free body diagram for the given system of forces.
Lect 22: At the end of lecture, learner will be able to calculate support reactions using conditions of equilibrium for beams.

## Slide 3: Introduction
A lamp hanging from the ceiling is an example of concurrent Force System in equilibrium.
Structures like buildings, dams etc. are examples of General Force System in equilibrium.
Students sitting on a bench is an example of parallel Force system in equilibrium.

## Slide 4
A force which is equal, opposite and collinear to the resultant of a concurrent force system
Equilibrant

## Slide 5: Types of Equilibria
Fig. 1 A body in a stable equilibrium[1]
A body is said to be in a stable equilibrium if
It is initially in a state of static equilibrium
and
On giving a slight displacement an additional
force is set up which tends to restore the
original position of the body.
Stable Equilibrium

## Slide 6: Unstable Equilibrium
A body is said to be in a unstable equilibrium if
It is initially in a state of static equilibrium
an additional force is setup on a slight displacement which tends to push it away from the original position of the body and
it does not return back to its original position after being slightly displaced by a force
Fig. 2 A body in an unstable equilibrium[1]
Types of Equilibria Cont..

## Slide 7: Neutral Equilibrium
A body is said to be in a neutral equilibrium if
it is initially in a state of static equilibrium,
no additional force is setup on a slight displacement from initial position and
it occupies a new position and remains in static equilibrium in this new position.
Types of Equilibria Cont..

## Slide 8: Conditions of Equilibrium
A body is said to be equilibrium if it is in a state of rest of motion.
(Based on Newton’s 1st Law of motion)
A body is said to be in equilibrium, if the resultant of the system
is zero

## Slide 9
Fig. 4 Ladder resting against a smooth wall[2]
A diagram formed by isolating the body from its surroundings and the showing all the forces acting on it is known as a Free Body Diagram
Free Body Diagram (FBD)

## Slide 10
Fig. 5 Lamp suspended from two strings tied to a ceiling[2]
Free Body Diagram (FBD)
Free Body Diagram Cont..

## Slide 11: Types of Supports

## Slide 12
Whenever a body is supported, the support offers resistance, known as reaction
Hinge Support
A hinge allows free rotation of the body but does not allow the body to have any linear motion.
It offers a force reaction which can be split: horizontal and vertical components
Fig. 6 Hinge Support[2]
Types of supports & Reactions
Types of Supports Cont..

## Slide 13: Hinge Support
A special case of Hinge Support: Internal Hinge or pin connection
When a two bodies are connected such that the connection allows rotation between the parts, and behaves as an hinge
Fig. 7 Scissors connected by a pin[2]
Types of Supports Cont..

## Slide 14: Roller Support
A roller support is free to roll on a surface on which it rests. It offers a forces reaction in a direction normal to the surface on which the roller is supported.
Fig. 8 Roller Support representation[2]
Types of Supports Cont..

## Slide 15
A fixed support neither allows any linear motion nor allows any rotation.
It therefore offers a forces reaction which can be split into a horizontal and a vertical reaction component and also a moment reaction.
Types of Supports Cont..
Fixed Support

## Slide 16
Offers similar reaction as a roller support
A force reaction normal to the smooth surface.
Fig. 10 Smooth surface Support representation[2]
Types of Supports Cont..
Smooth Surface Support

## Slide 17: Rope/string/cable Support
It offers a pull force in a direction away from the body.
This force is commonly referred to as the tension force.
Fig. 11 Lamp suspended by a two strings[2]
Types of Supports Cont..

## Slide 18: Types of loads
Fig. 12 Beams loaded with point load[2]
Point Load

## Slide 19: Uniformly distributed load (U.D.L.)
Types of loads Cont..

## Slide 20: Types of loads
Fig. 14 Beams loaded with u.v.l.[2]
Types of loads Cont..
Uniformly varying load (U.V.L.)

## Slide 21: Trapezoidal load
Fig. 15 Beams loaded with trapezoidal load[2]
Types of loads Cont..

## Slide 22: Types of loads
Fig. 16 Beams loaded with couple load[2]
Couple load
Types of loads Cont..

## Slide 23: Types of loads
Fig. 17 Beams loaded with couple load[2]
Varying load
Types of loads Cont..

## Slide 24: Equilibrium of single body Numerical
Q. 1 A beam is hinged at end A and roller supported at end B. It is acted upon by loads as shown. Determine the support reactions. (Ans. Ra = 16.06 kN, 49.69° Rb = 17.75 kN)
Fig. 18 Beams loaded with point load and u.d.l[2]

## Slide 25
Q. 2 A beam AB is loaded by forces and couples as shown. It is acted upon by loads as shown. Determine the support reactions to keep the system in equilibrium (HA = 11.54, Va = 16.02, Rb = 10.82, 600)
Fig. 19 Beams loaded with point, couple load and trapezoidal load[2]
Numerical on Equilibrium of single body Cont..

## Slide 26
Fig. 20 Bodies for F.B.D. [2]
Numerical on FBD Cont..
Q. 3) Draw F.B.D. for the following supported bodies in equilibrium. Take all plane as smooth

## Slide 27
Q. 4) Draw F.B.D. for the following supported bodies in equilibrium. Take all plane as smooth
Fig. 21 Bodies for F.B.D. [2]
Numerical on FBD Cont..

## Slide 28
Q. 5) A beam AB is loaded as shown. Determine the support reactions.
Fig. 22 Beam loaded with point load and u.d.l. [2]
Numerical on Equilibrium of single body Cont..

## Slide 29
Engineering Mechanics, N. H. Dubey, Mc Graw Hill Education (India) Pvt. Ltd.
Engineering Mechanics, M. D. Dayal, page no. 41 to 55.