## Slide 1: Engineering Mechanics Course code: 216U06C104 Module 3: Centroid of Wires and Lamina
3.1 Centroid of Wires/rods
3.2 Centroid of plane laminas: Plane lamina consisting of primitive
geometrical shapes.
Dr. Manish Deo
Assistant Professor
Department of Mechanical Engineering
Room – A301
e-mail – manish.deo@somaiya.edu
Mob. No. 97187960203

## Slide 2: Learning Outcomes
At the end of lecture learner will be able to calculate the centroid of the lamina

## Slide 3: Centre of Gravity of a body
Centre of gravity of body[1]

## Slide 4: METHODS FOR CENTRE OF GRAVITY
The center of gravity (or centroid) may be found out by any one of the following methods:
1. By Geometrical considerations, 2. By moments, 3. By graphical method

## Slide 5: Centre of Gravity of a body
Fig. 2 Centre of gravity of body[1]
The Centre of gravity is a theoretical point in the body where the body’s total weight is thought to be concentrated.
It is important to know the centre of gravity because it predicts the behaviour of a moving body when acted on by gravity.
It is also useful in designing static structures such as buildings and bridges.
In a uniform gravitational field, the centre of gravity is identical to the centre of mass. Yet, the two points do not always coincide.
For the Moon, the centre of mass is very close to its geometric centre. However, its centre of gravity is slightly towards the Earth due to the stronger gravitational force on the Moon’s near side.
https://www.youtube.com/watch?v=dxC_GuLNiAs&list=PPSV
https://www.youtube.com/shorts/BSvl7bgPLz4?feature=share

## Slide 6
Centre of Gravity vs. Centroid

## Slide 7: The plane figures (like triangle, quadrilateral, circle etc.) have only areas, but no mass. The center of area of such figures is known as centroid.
Fig. 3 Centre of gravity of flat plate[1]

## Slide 8: Important points
Centroid is the geometrical centre of the figure.
For the symmetric figure, centroid lies on the axis of symmetry.
If the figure is symmetric about X – axis, then
the y – coordinate of C.G. is
If the figure is symmetric about Y – axis, then the
x – coordinate of C.G. is
If the figure has more than one axis of symmetry then the
intersection of axis of symmetry is the centroid of the given figure.
Centroid may or may not lie on the given figure.
If the axis of symmetry is inclined at 450 to horizontal line then

## Slide 9: Important points

## Slide 13: Centroid of Sector of a circle
Fig. 6 Centroid of sector of a circle[1]
The location of centroid of the elementary sector A as shown in Fig. 4

## Slide 14: Numerical on Centroid of composite lamina
Fig. 7 Centroid of composite figure 5.88,3.91
Q. 1. Determine the centroid of the shaded portion.

## Slide 16
Fig. 8 Centroid of composite figure[2]
Q. 2. Determine the centroid of the shaded portion.
Numerical on Centroid of composite lamina

## Slide 18
Fig. 9 Centroid of composite figure[1]
Q.3. Determine the centroid of the shaded portion.
(A)
(B)
Numerical on Centroid of composite lamina

## Slide 19
Q. 4. Determine the centroid of the shaded portion.(Ans. X=7.98, Y=10.4)
Numerical on Centroid of composite lamina

## Slide 21
Q. 4. Determine the centroid of the shaded portion.
Ans: X= 18.46, Y= 35.13

## Slide 22
Q. 4. Determine the centroid of the shaded portion.
Ans: X= 9.176, Y= 6.937

## Slide 23: Centroid of composite lamina
A semi-circular section is removed from the plane area as shown. Determine the centroid of the remaining shaded section (Ans. X=0, Y= 9.239)

## Slide 25: Centroid of lines
Lines are one dimensional figures whose (L) is prominent than its thickness (b).
The thickness is also uniform throughout the length

## Slide 26: Centroid of lines
Lines are one dimensional figures whose (L) is prominent than its thickness (b).
The thickness is also uniform throughout the length
Imp note: Thickness b cancels out since it is uniform throughout the length.
The physical bodies which are equivalent to lines are bent up wires, pipe lines etc.
If these bodies are uniform throughout their length, then the centroid would coincide with the centre of gravity.

## Slide 27: Centroid of lines

## Slide 28: Centroid of lines

## Slide 29: Numerical on Centroid of lines
Q. 6 A thin homogeneous wire of uniform cross-section is bent into shape OABCO as shown. Determine its centroid.

## Slide 31
Q A thin homogeneous wire of uniform cross-section is bent into shape ABCDE as shown. Determine its centroid

## Slide 33: References
Engineering Mechanics, N. H. Dubey, Mc Graw Hill Education (India) Pvt. Ltd., page no: 5.1 to 5.26
Engineering Mechanics, M. D. Dayal, page no. 129 to 151.