## Slide 1
Name of Course: Engineering Mechanics
Course code: 216U06C104
Module 5: Kinetics of particles
Newton’s Law of Motion

## Slide 2: Syllabus: Module 5
5.1 Force and acceleration: Introduction to basic concepts, equations of dynamic equilibrium, Newton’s second law of motion (only rectilinear motion).
5.2 Work energy principle.
5.3 Impulse and Momentum: Principle of linear impulse and momentum, law of conservation of momentum, impact and collision, direct central and oblique central impact

## Slide 3: Learning Outcomes
At the end of lecture learner will be able to apply Newton’s second law of motion to solve numerical.

## Slide 4: Newton’s second law motion
Fig. 1 Forces acting at a point for a body[2]
Statement: The rate of change of momentum of a body is directly proportional to the resultant force and takes place in the direction of the force

## Slide 5: Newton’s second law motion
Fig. 1 Forces acting at a point for a body[2]
According to Newton’s second law motion
Rate of change of momentum = Resultant Force
i.e.
…….(5.1)

## Slide 6: Newton’s second law motion
The scalar relations for Newton’s second law of motion
………...(5.2 a)
……………(5.2 b)
…………..(5.2 c)

## Slide 7: Newton’s second law motion
D’Alembert’s Principle:
If the equation ΣF=ma is rearranged as
ΣF−ma=0,
treating the “– ma” as an inertia force, the system can be considered to be in dynamic equilibrium.

## Slide 9: Numerical on Newton’s second law of motion
Q. 1) A motorist travelling at a speed of 90 kmph suddenly applies the brakes and comes to rest after skidding 100 m. Determine the time required for the car to stop and coefficient of friction μk between the tyres and the road.[2]

## Slide 10: Numerical on Newton’s second law of motion
Q. 2) A 500 N crate kept on the top of a 150 sloping surface is pushed down the plane with an initial velocity of 20 m/s. If μs =0.5 and μk = 0.4. Determine the distance traveled by the block and the time it will take as it comes to rest. [2]

## Slide 11: Q. 2) A 500 N crate kept on the top of a 150 sloping surface is pushed down the plane with an initial velocity of 20 m/s. If μs =0.5 and μk = 0.4. Determine the distance traveled by the block and the time it will take as it comes to rest. [2]

## Slide 12: Numerical on Newton’s second law of motion
Q. 3) An elevator with a person inside, of total mass 500 kg starts moving upwards at a constant acceleration and attains a velocity of 3 m/s after traveling a distance of 3 m.
Determine :
i ) The tension in the cable
ii) If after attaining the velocity of 3 m/s the elevator stops in 2.5 seconds. Determine the pressure exerted by the elevator to the person weighing 600 N in the elevator.

## Slide 13: Numerical on Newton’s second law of motion
Q. 4) Three blocks A, B and C masses are 3 kg, 2 kg and 7 kg respectively are connected as shown. Determine the accelerations of A, B and C. Also determine the tension in the strings.[2]
Fig. 2 pulley supporting the loads suspended from a support[2]

## Slide 14: References
Engineering Mechanics, N. H. Dubey, Mc Graw Hill Education (India) Pvt. Ltd.
Engineering Mechanics, M. D. Dayal, page no. 41 to 55.

## Slide 15
Name of Course: Engineering Mechanics
Course code: 216U06C104
Module 5: Kinetics of particles
Lecture : Work energy Principle

## Slide 16
Work: It is defined as the product of the displacement and the force in the direction of the displacement.

## Slide 18
Work Done by Spring Force:
Consider a spring of stiffness k as shown in the figure, with some undeformed (free/original) length. Let x1 & x2 be deformations of spring at positions 1 & 2.
      Work done = Spring force × Deformation
∴ Spring force F = −k × x
where k is the spring stiffness (N/m) x is the deformation of spring (m) – ve sign indicates direction of spring force acting towards original position.

## Slide 19
Kinetic Energy: It is the energy possessed by a particle by virtue of its motion. K.E.=1/2*mv2
Potential Energy: It is the energy possessed by a particle by virtue of its position.
        P.E.=+mgh, if displacement is downwards
        P.E.=−mgh, if displacement is upwards
Work Energy Principle:
Work done by the forces acting on a particle during some displacement is equal to the change in kinetic energy during that displacement.

## Slide 21
Principle of Conservation of Energy:
Conservative Forces: If the work of a force is moving a particle between two positions is independent of the path followed by the particle and can be expressed as a change in its potential energy, then such forces is called as conservative forces. E.g., weight force of particle (gravity force), spring force and elastic force.
Non-Conservative Forces: The forces in which the work is dependent upon the path followed by the particles is known as non-conservative forces. E.g., frictional force
When a particle is moving from position 1 to position 2 under the action of only conservative forces (i.e., when frictional force does not exist) then by energy conservation principle we say that the total energy remains constant.

## Slide 25
Impact occurs when two bodies collide during a very short time period, causing large impulsive forces to be exerted between the bodies. Common examples of impact are a hammer striking a nail or a bat striking a ball. The line of impact is a line through the mass centers of the colliding particles. In general, there are two types of impact:
Oblique impact occurs when the direction of motion of one or both of the particles is at an angle to the line of impact.
Central impact occurs when the directions of motion of the two colliding particles are along the line of impact.
Impact

## Slide 26
There are two primary equations used when solving impact problems. The textbook provides extensive detail on their derivation.
Once the particles contact, they may deform if they are non-rigid. In any case, energy is transferred between the two particles.
Central impact happens when the velocities of the two objects are along the line of impact (recall that the line of impact is a line through the particles’ mass centers).
vA
vB
Line of impact
Central impact

## Slide 27
Central impact (continued)
In most problems, the initial velocities of the particles, (vA)1 and (vB)1, are known, and it is necessary to determine the final velocities, (vA)2 and (vB)2. So the first equation used is the conservation of linear momentum, applied along the line of impact.
(mA vA)1 + (mB vB)1 = (mA vA)2 + (mB vB)2
This provides one equation, but there are usually two unknowns, (vA)2 and (vB)2. So another equation is needed. The principle of impulse and momentum is used to develop this equation, which involves the coefficient of restitution, or e.

## Slide 28
Central impact (continued)
The coefficient of restitution, e, is the ratio of the particles’ relative separation velocity after impact, (vB)2 – (vA)2, to the particles’ relative approach velocity before impact, (vA)1 – (vB)1. The coefficient of restitution is also an indicator of the energy lost during the impact.
The equation defining the coefficient of restitution, e, is
(vA)1 - (vB)1
(vB)2 – (vA)2
e =
If a value for e is specified, this relation provides the second equation necessary to solve for (vA)2 and (vB)2.

## Slide 29
Coefficient of restitution
• Plastic impact (e = 0): In a plastic impact, the relative separation velocity is zero. The particles stick together and move with a common velocity after the impact.
• Elastic impact (e = 1): In a perfectly elastic collision, no energy is lost and the relative separation velocity equals the relative approach velocity of the particles. In practical situations, this condition cannot be achieved.
In general, e has a value between zero and one. The two limiting conditions can be considered:
Some typical values of e are:
Steel on steel: 0.5 – 0.8 Wood on wood: 0.4 – 0.6
Lead on lead: 0.12 – 0.18 Glass on glass: 0.93 – 0.95

## Slide 30
In a plastic collision (e = 0), the energy lost is a maximum, although it does not necessarily go to zero.
During a collision, some of the particles’ initial kinetic energy will be lost in the form of heat, sound, or due to localized deformation.
Once the particles’ velocities before and after the collision have been determined, the energy loss during the collision can be calculated on the basis of the difference in the particles’ kinetic energy. The energy loss is
 U1-2 =  T2 -  T1 where Ti = 0.5mi(vi)2
Impact: Energy losses

## Slide 31
Momentum of each particle is conserved in the direction perpendicular to the line of impact (y-axis):
mA(vAy)1 = mA(vAy)2 and mB(vBy)1 = mB(vBy)2
In an oblique impact, one or both of the particles’ motion is at an angle to the line of impact. Typically, there will be four unknowns: the magnitudes and directions of the final velocities.
Conservation of momentum and the coefficient of restitution equation are applied along the line of impact (x-axis):
mA(vAx)1 + mB(vBx)1 = mA(vAx)2 + mB(vBx)2
e = [(vBx)2 – (vAx)2]/[(vAx)1 – (vBx)1]
The four equations required to solve for the unknowns are:
Oblique impact

## Slide 32
• In most impact problems, the initial velocities of the particles and the coefficient of restitution, e, are known, with the final velocities to be determined.
• For oblique impact problems, the following equations are also required, applied perpendicular to the line of impact (y-dir.):
mA(vAy)1 = mA(vAy)2 and mB(vBy)1 = mB(vBy)2
• For both central and oblique impact problems, the following equations apply along the line of impact (x-dir.):
• Define the x-y axes. Typically, the x-axis is defined along the line of impact and the y-axis is in the plane of contact perpendicular to the x-axis.
Procedure of analysis
 m(vx)1 =  m(vx)2 and e = [(vBx)2 – (vAx)2]/[(vAx)1 – (vBx)1]

## Slide 33: Types of Collisions
A situation where the objects DO NOT STICK is one type of collision
Notice that in EACH case, you have TWO objects BEFORE and AFTER the collision.

## Slide 34: A “no stick” type collision
Spbefore =
Spafter
-10 m/s

## Slide 35: Types of Collisions
Another type of collision is one where the objects “STICK” together. Notice you have TWO objects before the collision and ONE object after the collision.

## Slide 36: A “stick” type of collision
Spbefore =
Spafter
5 m/s

## Slide 37: The “explosion” type
This type is often referred to as “backwards inelastic”. Notice you have ONE object ( we treat this as a SYSTEM) before the explosion and TWO objects after the explosion.

## Slide 38: Backwards Inelastic - Explosions
Suppose we have a 4-kg rifle loaded with a 0.010 kg bullet. When the rifle is fired the bullet exits the barrel with a velocity of 300 m/s. How fast does the gun RECOIL backwards?
Spbefore =
Spafter
-0.75 m/s

## Slide 39: Collision Summary
Sometimes objects stick together or blow apart. In this case, momentum is ALWAYS conserved.
When 2 objects collide and DON’T stick
When 2 objects collide and stick together
When 1 object breaks into 2 objects
Elastic Collision = Kinetic Energy is Conserved
Inelastic Collision = Kinetic Energy is NOT Conserved

## Slide 40: Elastic Collision
Since KINETIC ENERGY is conserved during the collision we call this an ELASTIC COLLISION.

## Slide 41: Inelastic Collision
Since KINETIC ENERGY was NOT conserved during the collision we call this an INELASTIC COLLISION.

## Slide 42: Example
Granny (m=80 kg) whizzes around the rink with a velocity of 6 m/s. She suddenly collides with Ambrose (m=40 kg) who is at rest directly in her path. Rather than knock him over, she picks him up and continues in motion without "braking." Determine the velocity of Granny and Ambrose.
How many objects do I have before the collision?
How many objects do I have after the collision?
2
1
4 m/s

## Slide 43
Name of Course: Engineering Mechanics
Course code: 216U06C104
Module 5: Kinetics of particles
Lecture 8: Impulse Momentum Principle

## Slide 44: Learning Outcomes
Lect 41: At the end of lecture learner will be able to apply impulse momentum principle to bodies getting impact.

## Slide 45: Impulse
Impulsive Force: A large force when acts for a very small time and which causes a considerable change in a particle’s momentum is called an impulsive force.

## Slide 46: Impulse momentum Equation

## Slide 47: Numerical on Impulse momentum principle
Q. 1 A block of mass 50 kg is placed on a plane inclined at 300 with the horizontal. A horizontal force of 250 N acts on the block tending to move down the plane. Determine its velocity 4 sec after starting from rest. Take μk = 0.3.

## Slide 48
Q. 2 A 630 gm cricket ball strikes the bat with a speed of 108 kmph and is hit back by batsman with a speed of 144 kmph. If the ball was in contact with the bat for 72 milliseconds. Determine the average impulsive force exerted on the ball. 612N

## Slide 53: References
Engineering Mechanics, N. H. Dubey, Mc Graw Hill Education (India) Pvt. Ltd.
Engineering Mechanics, M. D. Dayal, page no. 41 to 55.